SOP: checking the freesurfer segmentation for errors and correcting them

terminal command
name of a script/terminal command
path / filename

General information on freesurfer/correction: https://surfer.nmr.mgh.harvard.edu/fswiki/Edits

To start, use getserver -sL to connect to a compute server.
Here, type FREESURFER --version 6.0.0p1 in terminal, then type freeview for visualization program.
All the Scripts are in /data/pt_02030/freesurfer/QA/scripts/nipy1.4/qa/.
1. Subjects to be checked are found in SPSS-table /data/pt_02030/freesurfer/QA/QA_list.ods.
2. To get an overview over the data quality:
  0. edit subject ids to run the QA and run_freesurfer_qa.sh in the terminal	(./run_freesurfer_qa.sh)
    1. this will generate an output html in /data/pt_02030/freesurfer/QA/subj_id/rgb/snaps/subj_id.html
    2. have a look to this html

1. Issue 1: brain extraction (inclusion of skull into brainmask.mgz file) & possibly wrong surface placement (often due to bad brain extraction)
  check aseg and surfs row in the html to see whether the brain extraction was correct (e.g. no non-brain tissue appears in the aseg row, and red line in the surfs doesn’t include skull, dura mater or any part that is not brain.
  If you suspect that too much skull and non-brain tissue is included, type fslview /data/pt_02030/resting/structural/subj_id//transform_Warped.nii.gz /usr/share/fsl/data/standard/MNI152_T1_2mm_brain.nii.gz. Compare the two and see whether there are large amounts of non-brain tissue visible.
  If you see that the surface includes non-brain tissue, note degree of included tissue to 1. Note the result in the column Issue 1 (brain mask/pial surface) (0 – 1, no – major issue)
  Correct brain extraction (see https://surfer.nmr.mgh.harvard.edu/fswiki/FsTutorial/SkullStripFix_freeview, section on gcut)
  1.) open script freesurfer_correction.sh and perform steps one by one
      1. copy old freesurfer folder
      2. apply gcuts
      3. see result
      4. if this correction is too massive/little, try manual correction (if you have time :))
        open brainmask.mgz file and click on the “head with pen”-symbol in the left upper button row. Use the brush[1] as described in https://surfer.nmr.mgh.harvard.edu/fswiki/FsTutorial/PialEdits_freeview (set brush value to 255, eraser value to 0, then use SHIFT-button to erase voxels from brainmask which do not belong, when you're done, click on the “head with disk”, save volume button)
        [1] Use Voxel edit – Clone Voxel – reference: brain. For painting: brush = 0, eraser = 255; for erasing: brush = 255, eraser = 0
      5. if correction is done, note Issue 1 corrected (0 → not sucessful, 1 → sucessful)
      6. run autorecon-pial to recreate surfaces.
      7. Rerun preprocessing script to create correct brainmask for MNI registration
2. Issue 2: wrong white matter detection: white matter (especially in temporal lobes) is not detected as white matter and wm surface is wrongly placed.
  check surfs row in the html to see whether the wm surface (yellow) misses white matter. If the image is of low quality, also check full 3D view with freeview.
  To view the segmentation in freeview (and get a better impression), type
      1. FREESURFER in console
      2. type freeview
      3. click open volume and choose folder and select image (T1.mgz, brain.mgz, brainmask.mgz, aparc+aseg.mgz)
      4. click open surface to see lh.pial, rh.pial, lh.white and rh.white
      5. OR
      6. To see brain extraction issues, only show brain.mgz (with colormap “Heat”) and T1.mgz (and no surfaces!) → you will see skull included into brain volumetry
      7. To see white matter detection issues, only show brain.mgz and surfaces (lh.wm, rh.wm and maybe lh.pial, rh.pial)

Note the result in the column Issue 2 (white matter) (0 → no, 1 → yes)

Correct wrong white matter detection use control points (see https://surfer.nmr.mgh.harvard.edu/fswiki/FsTutorial/ControlPoints_freeview)
    1. open freeview to set control points (see freesurfer_correction.sh)
    2. set control points in freeview: Open New Point Set (File), name it control.dat, in brainmask und control points choosen!). If necessary to get a better impression, load asag.mgz + brain.mgz
    3. if necessary, improve contrasts with using brainmask.mgz and use: window, min, max-adjustments // + use aseg.mgz with setting “Lookup-Table”
    4. save control.dat in /data/pt_02030/freesurfer/subj_id/tmp/control.dat
    5. update freesurfer results
    6. Check intensity (white matter) correction:
      green/white (lower surfaces) are new boundaries and red/blue (upper surfaces) boundaries before correction
  1. Note the result in the column Issue 2 corrected (0 → not sucessful, 1 → sucessful)